## Slide 1: Smoke Tools and Information for Prescribed Fire and Wildfire
Types of Smoke Models (Theory)
Fire Emissions Calculation
Smoke Forecasting Systems
Smoke Tools
Satellite Information for Smoke and Fire
Putting on Your Smoke Glasses
Prescribed Burning in the WUI of Bend, Oregon
Photo – Ted Grussing

## Slide 2
Fire Location Information
Weather Model Output
Dispersion Model
Smoke Concentration Maps
Fire Emissions Model
Simple Approximation Systems
Trajectory Model
Smoke Plume
Location Approx.
Weather Observations
+
+
model complexity

## Slide 3
Simple
Plume
Trajectory
Types of Modeling
From Larkin et al. Smoke Prediction Tools
Examples:
Wind direction screening
Ventilation index
VSMOKE
HYSPLIT (trajectories)
FLEXTRA

## Slide 4
One-atm
Puff
Particle
One-atmosphere
Types of Modeling
From Larkin et al. Smoke Prediction Tools
Examples:
CALPUFF HYSPLIT (in puff mode)
SCIPUFF
HYSPLIT (in particle mode)
FLEXPART
CMAQ
WRF-CHEM
WRF-CMAQ
GEOS-CHEM
GEMMAQ

## Slide 6: BlueSky Smoke Modeling Framework Components to Calculating Fire Emissions
Fire Info
Fuels
Total Consumption
Time Rate
Emissions
Plume Rise
Smoke Modeling
SMARTFIRE2 NOAA HMS
GEOMAC
IRWIN
Rx Sys
Manual
Other
FCCS
FCCS-LF
NFDRS
Hardy
GVDS LANDFIRE Ag
Other
CONSUME
FOFEM FEPS
FLAMBE
FINN
Other
Rx / WF
FEPS FOFEM
EPM WRAP Other
FEPS Literature EPM FOFEM
FLAMBE
FINN Other
Briggs
FRP
Other
HYSPLIT,
CMAQ, VSMOKE
GEM-MACH
Large uncertainties exist with each modeling step
Meteorology
WRF
MM5
NARR
Station data

## Slide 7
Fire Info
Fuels
Total Consumption
Time Rate
Emissions
Plume Rise
Smoke Modeling
Large uncertainties exist with each modeling step
Meteorology

## Slide 8: Fuels Variability
Order of Magnitude
From: 2-10 tons/acre to > 100 tons/acre

## Slide 9: Meteorological Uncertainty
Wind Direction Mean Error
Day: 40 deg
Night: 80 deg

## Slide 10: PM2.5 Emission Factors
Urbanski 2014
FEPS
CONSUME
New Analysis
Emission Factor (EF): mass pollutant released per mass fuel consumed (e.g. g/kg)
Factor of 2 Variability

## Slide 11
Fire Info
Fuels
Total Consumption
Time Rate
Emissions
Plume Rise
Dispersion /
Trajectories
Fire Info
Fuels
Total Consumption
Time Rate
Emissions
Plume Rise
Dispersion /
Trajectories
Reality
Reality
right answer, wrong reasons
right answer, right reasons

## Slide 12: Smoke Model Online Resources (Forecast Systems)
BlueSky Daily Operational Runs http://www.airfire.org/data/bluesky-daily/
NOAA Air Quality http://www.nws.noaa.gov/airquality/ww.shtml
High Resolution Rapid Refresh (HRRR) – Smoke https://rapidrefresh.noaa.gov/hrrr/HRRRsmoke/
Canada – Firework https://weather.gc.ca/firework/index_e.html
Canada – BlueSky http://firesmoke.ca/
Northwest US – AIRPACT http://lar.wsu.edu/airpact/
Southeast US – HiRes2 https://forecast.ce.gatech.edu/
“Picking a model of choice for the day is a little like speed-dating: too little time/information to make up the mind leading to regrets by the end of the date/shift.”
- Wes Adkins, Meteorologist, National Weather Service, Juneau, AK
Notes: Links in Lesson Plan

## Slide 13: Tools for Wildfire and Rx Fire Smoke https://tools.airfire.org/

## Slide 14: Tailored Smoke Predictions Delivered to Incident Management Teams
Domains
  2-km CA/NV
  6-km Western US
  1.33-km WA/ID
  4-km PNW
  12-km CONUS
  12-km Alaska
  3-km CONUS
  1.8-km AZ/NM
  1-km FW (moveable)
Partnerships: NWS, UW, DRI, UofA
HYSPLIT – Primary near-surface 1-hr PM2.5
Notes: Partnerships!

## Slide 15: Tailored Smoke Predictions Delivered to Incident Management Teams
Fire Activity Information
NOAA Hazard Mapping System (HMS) Satellite Fire Detections
SmartFire v2 (SF2) augments (fire type, fire size, aggregation)
Notes: Partnerships!

## Slide 16
http://www.airfire.org/data/bluesky-daily/
Successful!
Running (click on “view logs” for run progress)
Number of Fires
Website shows status of current runs
Failures show up in red.
Notes: 12 domains per day, 6 are run twice a day (00Z, 12Z) – 18 hysplit particle runs. Many puff runs too.
This does not include custom runs.

## Slide 17: Daily BlueSky Production Runs 12/10/2017 Satellite Fire Detections & PM2.5, 6-km http://www.airfire.org/data/bluesky-daily/

## Slide 18: AIRPACT – Northwest
CMAQ
4-km
72-hours
Ozone, PM2.5
BlueSky Fire Emissions

## Slide 19: NOAA HRRR-Smoke (High Resolution Rapid Refresh)
Coupled Meteorology/Smoke (WRF-Chem)
3-km, CONUS, Alaska
Primary PM2.5
Visible Infrared Imaging Radiometer Suite (VIIRS)
  fire activity
  fire radiative power (FRP)
Plume Rise – FRP
Emissions – FRP
00Z, 06Z, 12Z, 18Z
36-hrs
https://rapidrefresh.noaa.gov/hrrr/HRRRsmoke/

## Slide 20: HRRR-Smoke Near-Surface PM2.5

## Slide 21: HRRR-Smoke Vertically Integrated PM2.5

## Slide 22: Firework – Canada
GEM-MACH
10-km
48-hrs
PM2.5 from only fires
CWFIS – Canadian Emissions
BlueSky – US Emissions
North America
Notes: GEM-MACH Air Quality Model
00Z, 12Z
Using CWFIS and BlueSky for fire emissions
Ozone too, but that is not publically available

## Slide 23: BlueSky Canada
BlueSky – Emissions and HYSPLIT
4-km, 12-km
48-hrs
CWFIS – Canadian Emissions
PM2.5 from fires
Notes: 12km national,
4km – west and east
HYSPLIT puff mode
00Z, 12Z

## Slide 24
Georgia Tech
Prescribed Burning
4-km Georgia
12-km CONUS
AQI, O3, PM2.5

## Slide 25: National Weather Service
HYSPLIT
CMAQ
Ozone, PM2.5
12-km
84-hours
BlueSky Fire Emissions

## Slide 26
“Picking a model of choice for the day is a little like speed-dating: too little time/information to make up the mind leading to regrets by the end of the date/shift.”
-Wes Adkins, Meteorologist, National Weather Service, Juneau, AK
(picked up by the Washington Post, Slate.com, and others)

## Slide 27: Trajectories https://tools.airfire.org/

## Slide 28: Smoke Trajectory Tool
Trajectories do not include:
  chemistry
  smoke dispersion
  heat released from the fire
A trajectory will appear the same whether a burn is 40 acres or 4000 acre
Simulates where a parcel of air would travel
Based on a 3-d meteorological description of the atmosphere
Plume rise simulated by above ground-level release height

## Slide 29: Smoke Monitoring Tool (Permanent and Temporary Monitors) https://tools.airfire.org/

## Slide 30: Monitoring Data Tool – Real-time PM2.5 Permanent and Temporary Monitors
https://tools.airfire.org/
Notes: Data as of 20171210 8am PST

## Slide 31: Monitoring Data Tool – Real-time PM2.5 Permanent and Temporary Monitors
https://tools.airfire.org/
Notes: Data as of 20171210 8am PST

## Slide 32: Monitoring Data Tool – Real-time PM2.5 Permanent and Temporary Monitors
https://tools.airfire.org/
Notes: Data as of 20171210 8am PST

## Slide 33: Monitoring Data Tool – Real-time PM2.5 Permanent and Temporary Monitors
https://tools.airfire.org/
Notes: Data as of 20171210 8am PST

## Slide 34: Satellite Information
NASA WORLDVIEW https://worldview.earthdata.nasa.gov/
Infusing Satellite Data into Environmental Applications (IDEAS) https://www.star.nesdis.noaa.gov/smcd/spb/aq/
Enhanced Infusing Satellite Data into Environmental Applications (eIDEAS) https://www.star.nesdis.noaa.gov/smcd/spb/aq/eidea/index.php
GOES-16 http://rammb-slider.cira.colostate.edu/?sat=goes-16&sec=conus&x=4999.95458984375&y=4999.95458984375&z=0&im=12&ts=1&st=0&et=0&speed=130&motion=loop&map=1&lat=0&p%5B0%5D=16&opacity%5B0%5D=1&hidden%5B0%5D=0&pause=0&slider=-1&hide_controls=0&mouse_draw=0&s=rammb-slider
Stay tuned for more
  GOES-16 Launched 11/2016 – in GOES East Position 11/2017
  NOAA-20 Launched 11/18/2017
  New/future GOES West – Launched March 2018
  TEMPO

## Slide 35: NASA Worldview 9/4/2017

## Slide 36: GOES-16

## Slide 37: GOES-16 9/4/2017 13:27 PDT

## Slide 38: GOES-16 9/4/2017 13:32 PDT

## Slide 39: Enhanced Infusing Satellite Data for Environmental Applications (eIDEAS)

## Slide 40
Notes: TODO: get GOES-16, do a CANSAC-2km analysis, 2017090300, 2017090312, 2017090400

## Slide 41: 9/4/2017 13:27 PDT
GFS
Column Average

## Slide 42: Putting on Your Smoke Glasses

## Slide 43: Carlton Complex Washington State 2014 250,000 acres
http://en.wikipedia.org/wiki/2014_Washington_state_wildfires
Notes: Use this example to talk about: grid resolution, comparing with monitoring data, timing of impacts and met models being off, calibrating your brain/experience
Example of: our production runs, how they get used by the ARA program for wildfires

## Slide 44: Carlton Complex August 2014
Washington Smoke Blog On this gorgeous, clear day with no smoke, let's take a look at the differences between two air quality monitors located less than 9 miles apart in the same Methow Valley. The blue graphs indicate 1-hr average concentrations of PM2.5 while the red data points are 24-hr averages. Note that while the 24-hr values trended rather similar for the two sites (expected as they are spatially close) the peak 1-hr values differed greatly!
Posted by Mike Broughton, FWS, ARA
Notes: Read the smoke blog to the class, then say, lets take it a step further and look at the models.
http://www.wasmoke.blogspot.com/search?updated-max=2014-08-18T11:08:00-07:00&max-results=8&start=4&by-date=false
Talk about 1-hr and 24-hr concentrations. NAAQS are a 24-hr std. Does smoke stay the same over a 24-hr period? Why or why not?
Use this example to talk about: grid resolution, comparing with monitoring data, timing of impacts and met models being off, calibrating your brain/experience
http://kcts9.org/programs/in-close/environment/wildfires-and-climate-change
http://kcts9.org/programs/in-close/environment/carlton-complex-progression-map

## Slide 45: Carlton Complex, 8/4/2014 6am, 1.33 km Domain
Winthrop
Twisp
Notes: Meteorology – what if it is off by 30 degrees?
The obs showed Twisp getting hit harder, yet BlueSky typically hit Winthrop harder – work in process

## Slide 46: Carlton Complex, 8/4/2014 6am, 12 km Domain
Winthrop
Twisp
Notes: Meteorology – what if it is off by 30 degrees? Does it matter so much with this resolution?

## Slide 47: Thank you
Special thanks to our funders in this work:
More information:
Sim Larkin larkin@fs.fed.us
Susan O’Neill
smoneill@fs.fed.us